## Slide 1
Ryan Beckett
with
Aarti Gupta, Ratul Mahajan, David Walker
A General Approach to Network
Configuration Verification
Notes: Today I’m going to be talking about a project I have been working on with … for verifying network control planes.
And when I say network control planes, what I mean is … BGP, OSPF as opposed to P4, OpenFlow

## Slide 2
Misconfigurations are common
Notes: misconfigurations in enterprise networks are quite common. For example, last year Southwest… led to grounding of 8000 flights, and there seem to be outages that wind up as top line news items every few months or so.

## Slide 3
Misconfigurations are expensive
$
$
Notes: In addition to being common, configurations are also expensive. Numerous studies that have looked at the problem have concluded that network outages caused by misconfiguration cost hundreds of thousands of dollars for every hour of downtime.

## Slide 4
Why control-plane configuration is hard
-BGP, OSPF, RIP
-Route redistribution
-Protocol preference
-Metric conversions
-Protocol parameters
-Interface metrics
-Route maps
-Access control lists
Complex
Low-level
Complexity
Distributed
Failures
-Device configurations
-100,000s of lines
-Link failures common
-Router failures possible
Failures
Distributed
Low-level
Bugs
Notes: A natural question then is:

## Slide 5
Current Approach: Simulation
Control Plane
Data Plane
Simulate
Traceroute
Inspect FIB
Data plane verification
Example: Batfish [Fogel et al, 2015]
Notes: Traditional operators don’t use verification
That may be changing with new tools like HSA, Veriflow
Still, there is simulation in the mix, because the control plane will be simulated

## Slide 6
Pure Simulation: Limitations
???
???
???
???
???
Must use a single,
fixed environment
Must use a single,
fixed set of failures
Often test for
particular packet(s)
Must use a single,
message ordering
1
2
Notes: Also, simulation is expensive, can typically only enumerate any 1 failure

## Slide 7
Current Approach: Heuristics
Configurations
interface int2_10 10.0.0.1/24
ospf interface int2_1
metric 1
ospf redistribute connected metric 10
redistribute connected
prefix-list PL_C 10.0.0.0/24
String Matching
Potential Issues
Example: rcc [Feamster et al, 2005]
Notes: Look for the presence or absence of certain strings

## Slide 8
Heuristics: Limitations
interface int2_10 10.0.0.1/24
ospf interface int2_1
metric 1
ospf redistribute connected metric 10
redistribute connected
prefix-list PL_C 10.0.0.0/24
String Matching
Unsound: can miss many bugs
Incomplete: can report false positives
Hard to test behavioral properties

## Slide 9
Verification Goal
We would like a scalable way to verify network properties for all possible data planes (packets, message orderings, environments, and k-failures)
‘‘
’’

## Slide 10
Verification Challenges
3
R1
R2
R3
2
1
Generality: directives are diverse and have complex interactions
Scalability: message ordering in the control plane matters
1
R1
R2
R3
2
3
≠

## Slide 11
Contributions
Encodes the network as a combinational circuit
Can model most control-plane features
and can verify a rich collection of properties
We build a tool called Minesweeper that:
in1
in2
out1
out2
Can scale to networks with hundreds of routers
using domain-specific optimizations that improve
performance over 460x
Uses an SMT solver to check properties for
all possible stable data planes.
Notes: Use this as a “rest of the talk” slide

## Slide 12
Minesweeper Architecture
Vendor-Independent Format
Cisco
Arista
Juniper
1.
Interfaces: {
Ethernet0/0: {
InterfaceCost: 1,
importPolicy: “PEER_IN”,
…
}
}
2.
Vendor-Specific Configs
3.
Combinational Circuit
Parse
Encode
4.
Property Violation
Query
ENV
Notes: Sucks in configs, generates formulas that represent stable solutions:
Mention easy to represent all environments here, just another input
Mention optimizations here

## Slide 13
Encoding Overview
R1
S1
S3
S2
N1
N2
N3
R2
R3
Does P hold in the network?
‘‘
’’
Network Encoding: N
Network Property: ¬ P
⋀
Satisfiable: Property Violation
Unsatisfiable: Holds for all stable data planes

## Slide 14
Network Representation
dstIp
srcIp
dstPort
srcPort
protocol
[0,232)
[0,25)
[0,28)
[0,232)
[0,216)
Data Plane Packet
controlFwdx,y
dataFwdx,y
1 bit
1 bit
Decision Process / Topology
failedx,y
[0,1]
prefix
prefixLen
adminDist
localPref
metric
ospfType
med
[0,232)
[0,25)
[0,28)
[0,232)
[0,216)
[0,232)
[0,22)
Control Plane Routing Record
origin
[0,3)
routerId
[0,232)
Notes: Can a “routing record“ reach this point in a stable solution Define term
Say that we are using either IDL or LIA

## Slide 15
Data plane packet
1
Running Example
}
dstIp
Symbolic Packet
srcIp:
dstPort
srcPort
[0,216)
[0,216)
[0,232)
[0,232)
protocol
[0,28)
{
R1
S1
S3
S2
N1
N2
N3
R2
R3
???
???
Notes: At the end of the day, we care about how a packet is forwarded through the network.

## Slide 16
Running Example
R1
S1
S3
S2
N1
N2
N3
R2
R3
S1
S3
S2
N1
N2
N3
OSPF
CON
BGP
BGP
OSPF
CON
OSPF
CON
R1
R2
R3
Protocol
View
Protocol Interactions
2

## Slide 17
Running Example
S1
S3
S2
N1
N2
N3
OSPF
CON
BGP
BGP
OSPF
CON
OSPF
CON
R1
R2
R3
Circuit
View for R1
Protocol Interactions
2
R1BGP
R1CON
R1OSPF
R2BGP
N1BGP
e1
e2
e3
e4
e5
e6
e7
out2
out3
out6
in1
in4
in5
in7
After R2
export filter
After R1
import filter
Redistribution
From CON to BGP
Notes: Can a “routing record“ reach this point in a stable solution Define term. Black dots are routing records.
“Convert view on left to circuit view. What it does is process routing records that can reach a particular point in the network in a stable solution.
For example, there is a routing record

## Slide 18
Running Example
R1BGP
R1CON
R1OSPF
N1BGP
e1
e2
e3
e4
e5
e6
e7
out2
out3
out6
in1
in4
in5
in7
med:
}
prefix:
Symbolic Record
prefixLen:
adminDist:
localPref:
[0,232)
[0,28)
[0,25)
[0,232)
metric:
[0,232)
[0,232)
ospfType
[0,22)
{
valid:
1 bit
Control Plane Info
3

## Slide 19
Import FIlters
4
Running Example
R1BGP
R1CON
R1OSPF
R2BGP
N1BGP
e1
e2
e3
e4
e5
e6
e7
out2
out3
out6
in1
in4
in5
in7
ip prefix_list L deny 192.168.0.0/16 le 32
ip prefix_list L allow
route-map R1_Import_From_R2 10
match ip address prefix-list L
set local-preference 120
R1 BGP import filter from R2
if e4.valid ∧ failedR1,R2 = 0 then if ¬ (FBM(e4.prefix, 192.168.0.0, 16) ∧
16 ≤ e4.prefixLen ≤ 32) then
    in4.valid = true in4.lp = 120 in4.prefix = e4 .prefix
    in4.metric = e4.metric
    in4.prefixLen = e4 .prefixLen
    …
else in4.valid = false
else in4 .valid = false
If message sent from R2
If it passes the import filter
Then R1 receives a message
with local-pref 120
SMT constraint
Otherwise, R1 does not
receive a message

## Slide 20
Decision Process
5
Running Example
R1BGP
R1CON
R1OSPF
R2BGP
N1BGP
e1
e2
e3
e4
e5
e6
e7
out2
out3
out6
in1
in4
in5
in7
(R1-BGP-Best.prefixLen < in1.prefixLen) ⋁
(R1-BGP-Best.prefixLen = in1.prefixLen ⋀
(R1-BGP-Best.localPref > in1.localPref) ⋁
(R1-BGP-Best.localPref = in1.localPref) ⋀
…
R1-BGP-BEST = Min(in1, in4, in5, in7)
R1-OSPF-BEST
R1-BEST = Min(R1-BGP-BEST
R1-CON-BEST)
Protocol Specific
Lexicographic Comparison (≤)

## Slide 21
Decision Process
5
Running Example
R1BGP
R1CON
R1OSPF
R2BGP
N1BGP
e1
e2
e3
e4
e5
e6
e7
out2
out3
out6
in1
in4
in5
in7
controlfwdR1,R2 = (in4 = R1-Best)
datafwdR1,R2 = controlfwdR1,R2 ⋀ ¬ ACL(R1,R2)
Does R1 forward to R2 in the control plane?
Does R1 forward to R2 in the data plane?

## Slide 22
Supported Features
OSPF Intra-area
OSPF Inter-area
eBGP Local-pref
eBGP Communities
eBGP MEDs
Implemented
Features
eBGP Aggregation
eBGP Path Prepending
iBGP
Route Reflectors
Static Routes
Route Redistribution
Multipath Routing
IPV6
Access Control Lists
Continued…

## Slide 23
Property: Reachability / Isolation
Can router R3 (not) reach subnet S2?
‘‘
’’
R1
S1
S3
S2
N1
N2
N3
R2
R3
canReachR2 ⇔ datafwdR2,S2
canReachR1 ⇔
    (datafwdR1,R2 ⋀ canReachR2) ⋁
    (datafwdR1,R3 ⋀ canReachR3)
canReachR3 ⇔
    (datafwdR3,R1 ⋀ canReachR1)
Property: canReachR3
Notes: Remind what the datafwd variable is here

## Slide 24
Property: Equal / Bounded Path Length
Do all routers in a pod have equal length paths to a destination port?
‘‘
’’
datafwdR1,R3 ⇒ lengthR1 = lengthR3 + 1
datafwdR2,R3 ⇒ lengthR2 = lengthR3 + 1
…
Property: lengthR1 = lengthR2
R1
R2
R3
Property: lengthR1 ≤ 4
Is the path length no more than 4?
‘‘
’’

## Slide 25
Property: Routing Loops
Can my network ever have loops?
‘‘
’’
throughR1,R1 ⇔
(datafwdR1,R2 ⋀ throughR2,R1) ⋁
(datafwdR1,R3 ⋀ throughR3,R1) ⋁
…
R1
R2
R3
throughR3,R1 ⇔
(datafwdR3,R1) ⋁
(datafwdR3,R2 ⋀ throughR2,R1) ⋁
Property: ¬throughR1,R1

## Slide 26
Property: Black Holes
Does router R1 ever black hole traffic?
‘‘
’’
R1
Property:
(dataFwdR4,R1 ⋁ dataFwdR5,R1 ⋁ …) ⋀
¬(dataFwdR1,R2 ⋁ dataFwdR1,R3 ⋁ …)
R2
R3
R4
R5

## Slide 27
Property: Multipath Consistency
Are multiple paths treated equally?
‘‘
’’
canReachR3 ⇒
(controlfwdR3,R4 ⇒
datafwdR3,R4 ⋀
canReachR3)
⋀
(controlfwdR3,R5 ⇒
datafwdR3,R5 ⋀
canReachR5)
…
R1
R2
R3
R4
R5
R6
Property:

## Slide 28
Properties
Do two routers serve equal roles?
‘‘
’’
Property:
(env1 = env2) ⋀ (env3 = env4) ⇒
(datafwdR1,R = datafwdR2,R)
⋀
R
R1
R2
env1
env4
env2
env3

## Slide 29
Properties
Is peer P1 preferred over P2 over P3?
‘‘
’’
Property:
env1.valid ⇒ datafwdR1,P1
¬ env1.valid ⋀ env2.valid ⇒ datafwdR1,P2
R2
R3
env1
env2
env3
P2
P1
P2
R1

## Slide 30
Properties
Does P hold after k link failures?
‘‘
’’
Constraint: ∑x,y failedx,y ≤ k
R2
R3
R1
Notes: Other properties such as path preferences, disjoint paths, load balancing, network equivalence

## Slide 31
Optimizations: Prefix Hoisting
med:
}
prefix:
Symbolic Record
prefixLen:
adminDist:
localPref:
[0,232)
[0,28)
[0,25)
[0,232)
metric:
[0,232)
[0,232)
ospfType
[0,22)
{
valid:
1 bit
FBM(r.prefix, 192.4.0.0, 16) ⋀
16 ≤ r.prefixLen ≤ 32
FBM(dstIp, 192.4.0.0, 16) ⋀
16 ≤ r.prefixLen ≤ 32
=
(192.4.0.0 ≤ dstIp ≤ 192.4.0.0 + 232-16) ⋀
16 ≤ r.prefixLen ≤ 32
=
Integer Difference Logic!
Notes: Set up mental model of what costs (prefix is a bitvector for every route record) (N representations of the control plane)

## Slide 32
Optimizations: Slicing
med:
}
Symbolic Record
prefixLen:
adminDist:
localPref:
[0,232)
[0,28)
[0,25)
metric:
[0,232)
[0,232)
ospfType
[0,22)
{
valid:
1 bit
Statically analyze the configs to
determine when certain attributes
are irrelevant
Example: if the local preference
is never explicitly set, then it can
not influence the decision process

## Slide 33
Optimizations: Slicing
Maintain a single copy of export
variables when the export policy
is uniform to all peers
Merge the import and export
records when the default import
policy is used
R1BGP
R2BGP
N1BGP
e2
e3
out2
out3
R1BGP
R2BGP
N1BGP
e2
out3

## Slide 34
Evaluation
Can Minesweeper find real bugs?
How well does Minesweeper scale?
1—23K lines of configuration
Compare verification time across a wide variety of properties
Test on a collection of synthetic data center benchmarks
Run on a collection of 152 legacy networks
Compare verification time with and without optimizations

## Slide 35
Evaluation: Bug Finding
Loopback0
R1
R2
Mangement interface reachability
Local equivalence of routers
Most required a specific environment
Found 67 violations of the property
Many caused by simple copy-paste errors
Found 29 violations
Example: BGP peer sends /32 with length 2
Example: ACL has missing entry

## Slide 36
Evaluation: Scalability
Management interface reachability
Local equivalence of routers
(For all n comparisons)
23K
1K
Lines of configuration
23K
1K
Lines of configuration

## Slide 37
Evaluation: Scalability

## Slide 38
Evaluation: Optimizations
Average speedup for an all-source
reachability query for data centers
Both with prefix hoisting alone,
and with network slicing added
Notes: It was very slow – BAD!
Change this to be more concrete

## Slide 39
Related Work
[1] Kazemian et al, NSDI’12
[2] Khurshid et al, NSDI’13
[3] Fogel et al, NSDI’15
[4] Feamster et al, NSDI’05
[5] Fayaz et al, OSDI’16
[6] Weitz et al, OOPSLA’16
[7] Gember-Jacobson et al, SIGCOMM’16
#Networks
#Dataplanes
Testing
Verification
HSA [1]
Veriflow [2]
Ping
Traceroute
Batfish [3]
ARC [6]
ERA [5]
Bagpipe [7]
Minesweeper
RCC [4]

## Slide 40
Conclusions
Encodes the control plane as an SMT formula
Can model a wide variety of features
Can verify a rich collection of properties
Minesweeper is a general and scalable control plane verification tool
Can scale to many real networks
in1
in2
out1
out2